### Switch Test Methodology

Switch testing:
1. Ssh access?
2. Core OS?
3. Do the switch talks openflow
4. Can it talk openflow+ssl
5. Works as with contoller learning switch?
6. Can you setup a backup/multiple controllers?
7. receives openflow messages?
  1. Features
  2. flow-mod
  3. send-packet
  4. read-state
  5. barrier
8. Flow mods behave as expected?
  1. Test with pings
  2. test with iperf
9. Jumbo Frames size?
10. SNMP access?
11. Has QoS?
  1. How can we enable it
  2. Does it interace well with openflow?
12. Has QnQ support?
  1. Does it work on openflow ports?
13. Is it sending events?
  1. Port status
  2. Packet-in
  3. Flow-removed
14. Performance effect of conulsilting the openflow tables
  1. per table
  2. per flow
  3. per port
  4. per queue
15. Throughput performance testing (can we really get 20GB per sec between two sites?).

Methodology:
1. SSH connect
2. Use the appropate tool
3. Configure a controller.
4. Configure a controller that tries to use ssl
5. Connect two hosts and try to ping between them
6. try to configure the redundant controller
7. On the controller, sen the messages and determine if the controller is following the protocol
8. Pings across hosts, iperf across hosts.
9. Increment MTU at test end point, try agin with iperf and ping tests.
10. Can we SNMP the device? If so can we get the IF-MIB table?
11. Check documentation, see how we can enable it.
  1. Verify QoS by iperf tests from the devices.
12. Check documentaiton.
  1. Try to send packes from the test nodes, check that the vlan tags (internal and external ) traverse the nodes correctly.
13. Check CPU usage while doing checks on each of the tables.
14. Put performance load on the devices.